## Slide 1: ELEC 7450 Term Project: Iterative Total Variation Deblurring
Spenser Burrows

## Slide 2: Motivation for deblurring
Blurring effects caused by improperly focused cameras or moving objects/cameras can greatly degrade the quality and usefulness of a digital image
Critical details can be lost due to blurring, and it’s not always possible to just take another picture

## Slide 3: Mathematical description of blurring
Blurring can be thought of as a convolution between an image and some blurring kernel that describes how a point source of light is transformed
Here, an image is blurred by blurring kernel
This process is also typically associated with random noise represented by , which prevents deblurring by a simple inverse filter

## Slide 4: Total Variation Regularization
In the early 90s, L. Rudin, S. Osher, and E. Fatemi proposed using an image’s total variation for image denoising, which can be defined as:
This can be used to correct for noise while preserving edges
This was soon adapted to the deblurring problem

## Slide 5: Total Variation Deblurring
The ROF method involves minimizing the following function with respect to :
The minimum in this function is the deburred image

## Slide 6: Gradient Descent
For this project, a fairly-straightforward and simple gradient descent method was selected to minimize
Gradient descent works iteratively, with each new iteration being defined as

## Slide 7
Each iterative step requires the numerical evaluation of the derivative of the total variation function shown below:

## Slide 8: Algorithm
Set as an initial guess for the image
Calculate
Calculate
Iterate until is below a set threshold, then return as the deblurred image

## Slide 9: Edge effects
Boundaries of the image can cause distortions due to the abrupt transition between an area with image data and the area outside the image

## Slide 10: Extrapolating to mitigate effects
Boundary distortions can be addressed by extrapolating the edges of the image out and dimming them gradually

## Slide 11: Testing
Known blurring kernels were used to artificially blur test images to evaluate the performance of the deblurring code

## Slide 12: LabVIEW GUI
To provide a user-friendly interface and open the possibility of integration with LabVIEW-controlled hardware, a LabVIEW virtual instrument was developed that interfaces with the MATLAB deblurring code

## Slide 13: About 44 seconds of iterations…

## Slide 14: Out of Focus Blurred Result

## Slide 15: Motion Blur

## Slide 16: Quantifying The Improvement
Abs(Original-Blurred) | Abs(Original-Restored)
12.8978 | 11.6557
11.0415 | 9.8693
10.3372 | 9.4154

## Slide 17: Motion Blurred F-14

## Slide 18: Motion Blurred F-14

## Slide 19: Out of Focus Blurred Lunar Surface

## Slide 20: Out of Focus Blurred Lunar Surface

## Slide 21: Summary
Total variation iterative deblurring is a very powerful technique for image restoration that is able to work even on noisy images
While there is room for improvement, this implementation is an effective tool that provides a user-friendly way to deblur images as long as information about the blurring kernel is known

## Slide 22: Questions?